## Slide 1: Network-wide Consensus Utilizing the Capture Effect in Low-power Wireless Networks
Proceeding
SenSys '17 Proceedings of the 15th ACM Conference on Embedded Network Sensor Systems
Article No. 1
Zhenyang Chao
05/03/2018

## Slide 2
Beshr Al Nahas -Chalmers University of Technology Gothenburg, Sweden
Simon Duquennoy
-RISE SICS, Sweden Inria Lille - Nord Europe, France
Olaf Landsiedel
-Chalmers University of Technology Gothenburg, Sweden

## Slide 3: Outline
Introduction
A2: agreement in the air
Evaluation
Conclusion

## Slide 4: Introduction
A2: Agreement in the Air
Based on Chaos
Basic concepts

## Slide 5: Low-power wireless network
cut down on overall power consumption
control the active time
varying the power setting modes of the devices
It is designed to allow long range communications at a low bit rate among things.
e.g. temperature sensors operated on a battery

## Slide 6: Capture effect
Capture effect is a phenomenon associated with FM reception in which only the stronger of two signals at, or near, the same frequency or channel will be demodulated.
Nodes overhearing the concurrent transmissions receive one of them with high probability, due to the capture effect.

## Slide 7: Network-wide Consensus
Networked cooperative robots
Wireless closed-loop control applications such as adaptive tunnel lighting
Industrial plants
...
Consensus is the problem of reaching agreement among several processes about a proposal, i.e., accept or decline it after a finite time of execution.

## Slide 8: Two simple consensus protocols
Two-phase commit(2PC)
(a) Proposal Voting
(b) Decide
simple, low complexity
limitation of being blocking
Three-phase commit(3PC)
(a) Proposal Voting
(b) Pre-Commit (or abort)
(c) Do Commit
non-blocking
unable to maintain consistency
One static coordinator(leader) and a set of participants(cohort)

## Slide 9: A2: agreement in the air
A set of network-wide communication primitives
Voting
2PC
3PC
Multi-phase
Join/Leave

## Slide 10: SYNCHROTRON
the synchronous transmission kernel
Slot
the minimum time unit, which fits one packet transmission or reception and processing, including packet handling by the application, authentication, en- and decryption, etc.
Round
grouped slots
VHT
virtual high-definition timer
maintains synchronization in A2 network

## Slide 11: Parallel Channels
Multiple channels in parallel are used In A2. Each node randomly chooses one channel per time-slot to either receive or transmit.
reduces network density and thereby increase the probability of capture
reduces network diameter
but increases frequency diversity...

## Slide 13
Voting Primitive
Nodes share two pieces of information in each transmission:
(a) The proposed value the nodes are voting on
(b) a list of votes representing for each node whether it already voted and whether the vote was for or against the proposal.
collects votes from all participants for or against a proposed value
the coordinating node is aware of which nodes voted for and against the proposal
so do other nodes

## Slide 14
Voting round

## Slide 15: 2PC in A2
handles node failures
a recovery mechanism
no further commit can complete until all blocked nodes are recovered

## Slide 16: 3PC in A2
There is a buffer state, pre-commit, between the voting and the commit phases, ensuring that no node commits while any other node is still uncertain.
Proposal Voting Phase
Pre-commit or Abort Phase
Do Commit Phase

## Slide 17: A2 Services
Join/leave
Sequence Numbers
...

## Slide 18: Join Request
Packet header
including low-level parameters such as length of the round, slot size, packet size, and when the next round is scheduled and its application type
New nodes
set a single bit join flag – in the packet header
Other nodes receiving this flag also set it in all subsequent transmissions.This flag will eventually propagate in the network and reach the coordinator, which will schedule a join round.

## Slide 19: Leave
If a node does not participate for a number of rounds, the coordinator distributes new flag assignments that remove the node from the list of participants.
Leave can optionally employ 2PC/3PC.

## Slide 20: Sequence Numbers
assign each configuration(node list) a sequence number, increased whenever nodes are added or removed
ensure consistency

## Slide 21: Evaluation
Testbed | Nodes # | Coordin-ator ID | Density # | Diam. [Hops] | Channel # | Tx Power [dBm] | Flags [Bytes]
Euratech | 213 | 3 | 106 | 2 | 15 | 0 | 27
Rennes | 190 | 3 | 90 | 2 | 15 | 0 | 23
Indriya | 97 | 35 | 32 | 3 | 2 | 0 | 13
Flocklab | 29 | 3 | 7 | 4 | 2 | 0 | 4

## Slide 22
Multiple channels

## Slide 23
Long-term performance
more than 21000 rounds for each testbed
average radio-on time for one round: 137–165 ms

## Slide 24
Consistency of Consensus
Vote has a low cost but suffers from inconsistencies, 2PC solves inconsistencies with blocking, 3PC trades consistency for liveness and maximizes the ratio of successful (live and consistent) transactions.

## Slide 25: Conclution
low-latency
reliable consensus
low loss rate

## Slide 26: Thank you!
E-mail: zhchao@ucsc.edu