## Slide 1
Presented by Andrea David
Authors: Seongmin Ham, Jihyung Lee, Kyunghan Lee
School of ECE, UNIST
QuickTalk: An Association-Free Communication Method for IoT Devices in Proximity

## Slide 2: IoT Device Implementation
Data processing service
IR and WiFi sensors

## Slide 3: Overview
Introduction
Related Work
System Design
Proposed Methods
Implementation
Evaluation
Conclusion

## Slide 4: Introduction
IoT devices are generally straightforward to use
There are some cases where usability is poor
  Visitor problem
    Alice visits her parent’s house and can’t change the settings on the IoT thermal controller
  Naming problem
    Bob wants to individually configure the many window shades in his office
  Range problem
    Charlie wants to publicize information to the passing-by users
Solution: QuickTalk

## Slide 5: QuickTalk
Association-free communication
Combines IR signal emission and WiFi overhearing
User device uses IR to pinpoint and ask the device for its ID
  e.g., WiFi MAC address
How to pinpoint a device in proximity?
How to set up a communication channel without an association process?

## Slide 6: Related Work
Network Architecture
Control Interface

## Slide 7: System Design
Problem Statement
  Users who don’t have permission can control the device
  Authorizing individual visitors is not secure
  Invalidating authorization is complicated
  Hard to identify which control interface corresponds to which IoT device
Solution
  Physically pinpoint an IoT device
  Control it at any direction

## Slide 8: Pinpointing
Candidates:
  IR, QR code, RFID, NFC, audio signal, and image processing
Requirements
  Few meters to tens of meters distance
  Minimal effort
  Maximum accuracy

## Slide 9: QuickTalk Architecture
Two services
  IR pinpointing
  WiFi service for communication
User Device
IoT Device

## Slide 10: QuickTalk Workflow

## Slide 11: Challenges
Pinpointing ability of IR signal in real IoT environments
  Reachable distance
  Angle for pinpointing
  Information bits (length, type, channel coding)
Implementation of WiFi communication
  Association-free WiFi comuncation
  No authentication
  Security protection?

## Slide 12: Proposed Methods (IR Pinpointing)
Identify IoT device to control
Trigger WiFi interface for communication

## Slide 14: Proposed Methods (WiFi Communication)
Fake power save poll (802.11 standard)
Packet broadcast, monitoring

## Slide 16: User Device Implementation
  User interface
  IR and WiFi Services

## Slide 17: Security Implementation
IR signal emits encryption key from user device
IoT device authenticates key and ID
Elliptic Curve Menezes-Vanstone

## Slide 18: Evaluation

## Slide 19: End-to-end Delay

## Slide 21: Coexistence with Ongoing Sessions

## Slide 22: Conclusion
Visitor, naming, distance problem
Intuitive
Pinpointed communications for IoT devices